## Slide 1: Solar Installation Optimization in Colorado
Jaswanth Das Gunturu
Aditya Gidda
Gregory Howard
Bhavya Kavuri
Udaya Mutyala

## Slide 2: Contents
Introduction
Information Gathered
Assumptions
Optimization Setup
Results/Test Cases
Conclusions
References

## Slide 3: Introduction
Climate change
Solar = effective solution
Costs vary geographically
  Efficiency as well
Transmission costs
  Solar farms vs residential
Colorado 50% renewable
revisionenergy.com

## Slide 4: Information Gathered
Existing solar resources and their installation costs
  NREL Open PV Project
Solar Panel Sizing
  250 W per 16.5 square feet
Transmission Costs
  Expensive per mile ($285,000)
Maintenance Costs
  1% per year of development costs
Sun Light Hours
  Average in Colorado of usable light (1348 hours)

## Slide 5: Assumptions
District 6 - Large Population
District 5 - Less Sunlight Due to Mountains
District 7 - Existing Large Solar Developments

## Slide 6: Assumptions
Size of solar panel - 250W
Locations of the Solar Farms
  Distance from one division to another transmission
  1% loss per 100 miles
7% loss for transmission and distribution
Impact of Temperature and weather not taken into consideration
1% development cost per year
Missing values of cost have been imputed by average values of remaining
Land acquisition cost ignored

## Slide 7: Optimization Setup
Linear Programming Model in AMPL
Variables
  Solar Generation/District
  Transmission to Neighboring Districts
Variable Weights
  Transmission Losses
    Distance and Average
  Sunlight Hours per District
  Maintenance Costs
Objective Function
  Cost of Development and Transmission
Constraints
  Energy = Demand for each district
  Non negativity for generation and transmissions

## Slide 8: Results/Test Cases

## Slide 9: Results/Test Cases
Transmission cost of 2.4 Thousand $/kW upper bound
  Electricity generated in all districts
Transmission cost of 0 generates electricity in districts 1, 6 and 8
  Transmission losses still affect generation
Approximate cost of transmission of 1.65 Thousand $/kW
  Assuming 15 miles required transmission and the average districts’ energy needs
  Within range of used values
Notes: Some of the interesting points in the sensitivity testing of the model
Upper bound where transmission costs are so high that no transmission is picked by the model
Even at zero transmission costs the transmission efficiencies affect the model as losses cause more generation therefore no district ever produces all energy
Approximate cost of transmission fall within range of our tested values meaning that it is important

## Slide 10: Conclusions
Complexity increases quickly
  Initially considered all counties individually
Model selects either all or nothing
  Cost differences between generation and transmission
Model needs built in costs for cheap interconnection
  Forces residential development
Costs were inflated
  National cost average ($2.8/W) and Colorado cost average ($7/W)
  Over two times increase
  $103 billion Colorado and $41 billion national
Colorado Needs More Solar
  Current 0.3 sq. miles increase to 49 sq. miles (104,185 sq. miles in CO)
Notes: Complexity - all counties, weather, transmission losses vary by area as well
All or Nothing - When differences in generation costs are reached by transmission costs then districts generate all their own
Currently a district could produce no energy even though costs of residential development can be very low in some situations
Costs were over two times higher than expected given national average
I

## Slide 11: References
https://news.energysage.com/250-watt-solar-panels-are-they-right-for-you/
https://openpv.nrel.gov/
https://en.wikipedia.org/wiki/Electric_power_transmission
https://www.elp.com/articles/powergrid_international/print/volume-18/issue-2/features/underground-vs-overhead-power-line-installation-cost-comparison-.html
http://insideenergy.org/2015/11/06/lost-in-transmission-how-much-electricity-disappears-between-a-power-plant-and-your-plug/
http://www.longtermsolar.com/solar-sunlight-hours-in-colorado/
https://www.nrel.gov/docs/fy17osti/68281.pdf

## Slide 12: THANK YOU